## Slide 1: CAD Design Similarity Search
LATENTVIEW ANALYTICS | INDUSTRIALS | REFERENCE DOCUMENT
Retrieval of structurally similar designs from a CAD repository using B-Rep embeddings from BRepNet and vector search with FAISS
GenAI for CAD | Proof of concept
Vishal Prabu | October 2026
Notes: Reference deck for the CAD shape similarity search proof of concept. Covers the method, the library modifications required to run BRepNet on current software, the results, the added capabilities, and how to use the repository.

## Slide 2: Project overview and objectives
OVERVIEW
Problem
Design repositories grow large, and locating an existing part that resembles a new one usually depends on file names, metadata or recall. Reuse opportunities are missed and near-duplicate parts are redesigned.
Approach
A query part supplied as a STEP file is converted into a numerical embedding. The nearest embeddings in an indexed repository identify the most structurally similar designs. Query is by example part; text-to-shape search is not part of this pipeline.
Objectives
1
End-to-end retrieval pipeline for B-Rep CAD models using open-source tools.
2
Embeddings from native B-Rep topology with a pretrained model, without retraining.
3
Ranked results with distance scores and part properties for every match.
4
Size-aware filtering and search by a newly supplied STEP file, delivered through a web interface.
Data source. Fusion 360 Gallery Reconstruction Dataset (Autodesk Research): 500 final-stage designs sampled with fixed seed 42. The licence permits non-commercial research use only; client-facing or commercial use requires a separate licence review.
CAD Design Similarity Search | Reference document
2
Notes: Purpose of the project and the scope of the proof of concept. Similarity here means feature composition (mix of extrusions, fillets, chamfers and similar), not size or proportions.

## Slide 3: Pipeline and technology stack
METHOD
01 Parse
STEP to B-Rep
occwl 3.0.0 on pythonocc-core 7.7.0 reads the STEP file through OpenCascade and exposes faces, edges and coedges.
02 Embed
BRepNet
Pretrained BRepNet passes messages over coedges. The 84-dimensional per-face hidden layer before the classifier is extracted.
03 Pool
Mean pooling
Per-face vectors are averaged into one 84-dimensional embedding per part, stored as embeddings.npy (500 × 84, float32) with a filename manifest.
04 Search
FAISS
IndexFlatL2 performs exact Euclidean search. Brute force is sufficient at 500 vectors; approximate indexes apply only at much larger scale.
Technology stack
Python 3.10
conda-forge environment brepnet
pythonocc-core 7.7.0
OpenCascade bindings
occwl 3.0.0
B-Rep API, built from source
BRepNet (patched)
pretrained, inference only
PyTorch 2.14.0 (CPU)
model inference
PyTorch Lightning 2.6.5
BRepNet runtime
faiss-cpu 1.15.1
vector index
Streamlit 1.65.0
web interface
CAD Design Similarity Search | Reference document
3
Notes: BRepNet is a topology-based message-passing network (coedge convolution), not a transformer. Mean-pooling the per-face hidden representation gives one vector per part. CadQuery is deliberately not installed in the brepnet environment because it bundles its own OpenCascade.

## Slide 4: Modifications to third-party libraries
MAINTENANCE
The environment file shipped with BRepNet targets Python 3.7, PyTorch 1.7.1 and PyTorch Lightning 1.5.10. The changes below to the vendored copy in external/BRepNet allow it to run on Python 3.10, PyTorch 2.14.0 and PyTorch Lightning 2.6.5.
File or component | Change and reason
models/brepnet.py | LightningModule import path updated for current PyTorch Lightning.
models/brepnet.py | test_epoch_end migrated to on_test_epoch_end(), as the old hook was removed.
eval/evaluate_folder.py | Argparse-based Trainer setup replaced with Trainer(accelerator="cpu", logger=False).
Checkpoint loading | torch.load patched with weights_only=False, since newer PyTorch defaults to weights-only loading. The pretrained checkpoint is trusted.
pipeline/extract_brepnet_data_from_step.py | Per-file try/except added, so one unreadable STEP file no longer stops a batch run.
run_batch_embeddings.py (new) | Copies STEP files to a scratch folder, runs evaluate_folder, mean-pools per-face embeddings and writes embeddings.npy and embeddings_manifest.json.
occwl dependency | Internal submodule reference (git.autodesk.com) replaced by public occwl 3.0.0 built from source (not on PyPI). pyDeprecate (pip) and igl (conda-forge) added.
CAD Design Similarity Search | Reference document
4
Notes: These edits apply to the vendored copies of BRepNet and occwl under external/. Anyone rebuilding the environment must use the vendored BRepNet copy rather than upstream, otherwise the Lightning API changes cause failures.

## Slide 5: Retrieval results
RESULTS
Query: 100243_9fb796fe_0006 | 130 × 19 × 19 mm | 6 faces
Rank | Design ID | Squared L2
1 | 37267_b2be4b50_0033 | 0.0397
2 | 33628_296ae2b8_0001 | 0.0630
3 | 37995_1cc61263_0005 | 0.1063
4 | 105278_909f3813_0000 | 0.2123
5 | 86381_dcef1ea4_0000 | 0.2308
Rank 1 is a thick bar (1100 × 75 × 75 mm) matched to a thin column: feature composition is similar, size is not. Smaller distance indicates a closer match.
Validation. Re-embedding parts already in the index reproduced the stored embedding rows within about 1e-7. Retrieval was also spot-checked visually: simple parts retrieve well, while complex parts are less consistent (see limitations).
CAD Design Similarity Search | Reference document
5
Notes: Unfiltered top-5 for the example query. Distances are squared Euclidean (L2) values as returned by FAISS IndexFlatL2 in the 84-dimensional embedding space. Insert thumbnails from data/processed/fusion360_subset (each STEP file has a matching PNG) or from notebooks/inspect_retrieval.ipynb.

## Slide 6: Capabilities beyond basic retrieval
CAPABILITIES
part_properties.py
Part size properties
Bounding-box dimensions, volume, surface area and face count per part from occwl, stored in part_properties.csv.
filtered_search.py
Optional size filter
Sorted bounding-box dimensions must fall within a tolerance of the query (default ±20%). All 500 designs are searched, then survivors are ranked.
search_new_part.py
New-part search
An uploaded STEP file is embedded through the same pipeline and searched against the index. Test part: 24 × 24 × 4.5 mm, top distances 0.2087 to 0.4556.
app.py
Streamlit interface
Choose an existing part or upload a STEP file, set the size filter and tolerance (5 to 50%), and review top-5 match cards.
CAD Design Similarity Search | Reference document
6
Notes: Match cards in the app show a thumbnail, distance and part properties. When no design falls within the tolerance the app shows a "No matches within tolerance" message. Unreadable STEP uploads are rejected before embedding. Filter example for query 100243_9fb796fe_0006: 22124_6f71410e_0010 (25.7549) and 24470_21c25a2d_0002 (27.4739). New-part example filtered matches: 40800_7fa2d7a5_0000 (17.1243) and 22124_6f71410e_0011 (23.0212).

## Slide 7: Repository and usage
USAGE
GitHub repository
Placeholder: confirm the final repository location before circulation.
git clone https://github.com/vishalprabu-lab/shape-similarity-search.git
Environment setup
# brepnet: embeddings, properties, app
conda create -n brepnet python=3.10 -c conda-forge -y
conda activate brepnet
conda install -c conda-forge pythonocc-core=7.7.0 igl -y
pip install torch --index-url https://download.pytorch.org/whl/cpu
pip install pytorch-lightning==2.6.5 pyDeprecate
pip install faiss-cpu streamlit
pip install ./external/occwl
# .venv: subset, index, basic query
python -m venv .venv
.venv\Scripts\activate.bat
pip install -r requirements.txt faiss-cpu
Run order
python inventory_data.py
src/, .venv: build the 500-design subset
python run_batch_embeddings.py
external/BRepNet/, brepnet: embeddings
python build_faiss_index.py
src/, .venv: FAISS index
python src/part_properties.py
root, brepnet: part_properties.csv
streamlit run app.py
root, brepnet: web interface
CAD Design Similarity Search | Reference document | The Fusion 360 Gallery data is downloaded separately
7
Notes: Commands follow the repository README and should be re-checked against it after any change. The dataset (Fusion 360 Gallery Reconstruction) is not redistributed with the repository and is expected under data/raw/fusion360gallery/reconstruction/. run_batch_embeddings.py contains hardcoded paths and writes directly to outputs/embeddings.npy, so paths must be checked before re-running. The notebook notebooks/inspect_retrieval.ipynb provides visual inspection of a query and its top matches.

## Slide 8: Limitations and further use
OUTLOOK
Known limitations
Similarity is not size. Matches share feature composition, so a thin column can match a thick bar. The size filter corrects this, but filtered matches lie far in embedding space (distance 17 to 27, against 0.04 to 0.5 unfiltered).
Complex parts. Retrieval is less consistent on geometrically complex parts. Mean pooling of per-face embeddings is the suspected cause; not yet root-caused.
Malformed STEP files. A file that loads but is malformed can crash pythonocc inside the BRepNet pipeline. Unreadable files are rejected before embedding; malformed ones are not.
Scope and licence. The index covers 500 designs, including some unit-scale outliers. The Fusion 360 Gallery data is licensed for non-commercial research only.
Further use and next steps
Design reuse. Query the repository with a new part before modelling, to find existing designs to reuse or adapt.
Duplicate detection. Very small distances flag candidate near-duplicate designs for review.
Feature-aware search. The same BRepNet backbone supports machining-feature recognition. Predicted features can complement embeddings for ranking and filtering.
Retrieval quality. Evaluate alternatives to mean pooling on complex parts, and move to an approximate FAISS index if the repository grows substantially.
Evaluation on in-house CAD data, where licensing and data access permit.
CAD Design Similarity Search | Reference document
8
Notes: Limitations are stated as observed during the proof of concept. Retrieval quality on complex parts has not been quantified with a formal benchmark; assessment so far is by manual visual spot-checks.